## Slide 1: Storage and Virtualization for the DBA
Everything you should know but don’t want to.
Denny Cherry MVP, MCDBA, MCSA, MCTS, MCITP
Senior Database Administrator
Phreesia

## Slide 2: About Me
Author or Coauthor of 4 books
6+ SQL Mag articles
Dozens of other articles
Microsoft MVP since Oct 2008
12 Microsoft SQL Certifications
  1 of 2 MCM Test Completed (go me)
Sr. DBA for Phreesia

## Slide 3: I love questions
Try and keep them on point…
We can always chat during lunch or after the session…
Remember…
  There’s no such thing as a dumb question…
  But don’t take it personally if we all laugh anyway.

## Slide 4: Just to be clear …
Any Questions?
I have, on occasion said a word or two that some might find offensive. Those of a delicate nature, may wish to run screaming from the room at this time…

## Slide 5: Topic Highlights
Storage Arrays – 60% of today
Storage Networks – 20% of today
Virtualizing SQL Servers – 20% of today

## Slide 6: Todays goal is to prevent this from happening.

## Slide 7: Storage Array Agenda
Storage Terminology
Array Cache Setup
RAID Types
Spindle Types
Tiered Storage
Disk Alignment
Physical Array Diagram
Array Design Differences
Snapshots, Clones
Array Based Replication
Multipath IO Drivers
Thin LUNs
Monitoring
Power Up / Power Down

## Slide 8: Storage Terminology
LUN = Logical Unit Number
Host = The Server or Servers a LUN is presented to
SAN = Storage Area Network
Disk = How the OS sees a LUN when presented
Fabric = Network which makes up the SAN
Spindle = Physical disks in the Storage Array
Array = Box with the Spindles in it
HBA = Host Buss Adapter

## Slide 9: Storage Terminology
Throughput = Measured in Megs Per Second
IOps = Physical Operation To Disk
Sequential IO = Reads or writes which are sequential on the spindle
Random IO = Reads or writes which are located at random positions on the spindle
Front End Ports = Ports between servers and array controllers
Back End Ports = Ports between array controllers and spindles

## Slide 10: Cache Setup
OLTP databases make poor use of SAN read cache
OLAP databases make good use of SAN read cache
Try reducing read cache and increasing write cache
OLTP databases with high buffer cache hit ratios may be able to have the read cache disabled
There is no one correct setup. Every system is different.

## Slide 11: When Write Cache Gets Full?
Doesn’t flush to disk until low watermark is hit
Force flushes once high watermark is hit
Force flushing completely empties write cache
Force flushing disables write cache until write cache is disabled
If adjustable, set low very low, and high watermark very high (20/90)
If cache gets to 100% full – Pray!

## Slide 12: Oh crap the power went out!
Most arrays have internal batteries
Write cache is flushed to disk
After flush array powers down
On power-up flushed cached is read and committed to LUNs before LUN is made available
Make sure SQL is down before the array flushes
http://www.flickr.com/photos/robertfrancis/352039299/

## Slide 13: EMC Physical Diagram

## Slide 14: Flash Cache
Being introduced by some vendors
Either EFDs or flash card used as secondary cache
High cost
High performance
Some vendors provide redundancy with cache, some don’t.
Some vendors provide for read only, some read write

## Slide 15: RAID Types – RAID 1
Full Mirror of data
No performance Benefit
High Cost
Requires 2 disks
Can survive 1 disk failure

## Slide 16: RAID Types – RAID 0+1
Drives Striped, then Stripes Mirrored
High Cost
High Performance
Requires 2 disks
Requires an even number of disks
Can survive 1 spindle failure
May survive multiple spindle failure

## Slide 17: RAID Types – RAID 10
Also Known As 1+0
Drives Mirrored, then Mirrors Striped
High Cost
High Performance
Requires 2 disks
Requires an even number of disks
Can survive 1 spindle failure
May survive multiple spindle failure

## Slide 18: RAID Types – RAID 5
Stripe with single parity drive
Low cost
Good performance
Write penalty
Can survive a single drive failure
Requires at least 3 disks

## Slide 19: Not all RAID 5 is Created Equal
RAID 6 can be done this way as well.

## Slide 20: RAID Types – RAID 6
Stripe with two parity drives
Slightly higher cost per gig than RAID 5, good performance
Same write penalty as RAID 5
Can survive 2 disk failures
Requires at least 4 disks

## Slide 21: RAID Types – RAID 0
Straight Stripe
No redundancy
Very fast
Low cost
Any disk failure looses data
Can not survive any disks failures
Requires 2 or more disks

## Slide 22: What’s the correct choice?
Logs, TempDB – RAID 1, 10, 0+1
System Databases – RAID 5, 6
Backups – RAID 5, 6
User Data – RAID 5
Indexes – RAID 5

## Slide 23: When to switch RAID types
From 5 to 10 (or 0+1)?
  Over 10% data change (30% on EMC storage)
  High writes
  Cache is force flushing
From 5 to 6?
  Disks fail often

## Slide 24: Beware The High Capacity Spindles
High capacity spindles are awesome, until they fail
Large spindles get filled and are busy
Failed spindles take time to rebuild
146 GB spindles in a 14 spindle RAID 5 can take ~12 hours
1 TB spindles in a 14 spindle RAID 5 can take 1-2 days

## Slide 25: Read vs. Write Comparisons

## Slide 26: Spindle Types
Enterprise Flash Disks (EFDs)
  Newest Technology
  4 Gig Buss Speed
  Up to 30k IO per spindle
Fiber Channel (FC)
  2-4 Gig bus speeds
  10k-15k RPM
  Up to ~300 IO per spindle

## Slide 27: Spindle Types
SCSI
  Older Technology
  1-2 Gig Bus Speed
  Up to 200 IO per spindle
  Up to 10k RPM
SATA
  Newer Technology
  1-4 Gig buss speed
  Up to 200 IO per spindle
  7200 RPM

## Slide 28: Tiered Storage
Time is Money
http://www.flickr.com/photos/21560098@N06/3832712784/

## Slide 29: Tiered Storage – Tier 0
Enterprise Flash Disks low capacity drives
Very high cost
Very high speed storage
Great for Databases
http://commons.wikimedia.org/wiki/File:Speedometer_Odometer.jpg

## Slide 30: Tiered Storage – Tier 1
15k RPM Fibre Channel low capacity drives
High cost, high speed storage
Great for Databases, Exchange, Virtual Machines
http://commons.wikimedia.org/wiki/File:Speedometer_Odometer.jpg

## Slide 31: Tiered Storage – Tier 2
10k RPM Fibre Channel medium capacity drives
Medium cost, medium speed storage
Great for File Servers, Database Archives, Exchange
http://commons.wikimedia.org/wiki/File:Speedometer_Odometer.jpg

## Slide 32: Tiered Storage – Tier 3
7.2/5.4k RPM SATA/SAS high capacity drives
Low cost, low speed storage
Great for Backups, Archives, Exchange
http://commons.wikimedia.org/wiki/File:Speedometer_Odometer.jpg

## Slide 33: Disk Alignment

## Slide 34: Disk Alignment
Can improve SQL disk performance up to 100%
  (64 1k blocks/64k IO)=100% of IO is impacted
Must be done before data is put on the disk
Windows 2000 - Diskpar
Windows 2003 - Diskpart
Windows 2008 - Automatic

## Slide 35: Buss Speeds
Front end ports – 2-8 Gigs
  Ports the clients use to connect to the storage array
Back end ports – 1-20 Gigs
  Ports the controller uses to talk to other components within the array
http://www.flickr.com/photos/laffy4k/88841552/

## Slide 36: Array Diagram

## Slide 37: Different Storage Array Design Techniques
Shared Everything (RAID 10)
Shared Everything (RAID 6)
Shared Some with Admin Control
No RAID arrays

## Slide 38: Shared Everything (RAID 10)
3PAR
Each pair of disks is a RAID 1 array
Use Lots of Disks
Data on Disks is a chunk
Create LUNs as (disks*chunk size)
One disk slows down, everything slows down
No Parity Calculations

## Slide 39: Shared Some with RAID 6
NetApp
Each shelf is a RAID 6 Array
Each write has two parity calculations
One LUN slows down, everything on the shelf slows down.
Easy to manage

## Slide 40: Shared Some Array
EMC, Hitachi, Some IBM Units
High Management Overhead
Total Control of LUN placement
LUN can span RAID groups

## Slide 41: No RAID Storage Arrays
IBM XIV
Disk shelves are either IO modules or disk modules
Data is placed on one IO module and one disk module
LUNs are created in 1 Meg chunks on as many disks are needed to create the LUN.
Can survive multiple disk failures
Can survive multiple shelf failures
If the right two disks fail, a LUN can become corrupt

## Slide 42: No RAID Storage Arrays
How the data is written

## Slide 43: Array Snapshots
Similar to SQL Server Snapshots
A consistent point in time snapshot on a LUN
Can be mounted to other servers in read or read/write mode
Requires that host disks be flushed before snapshot can be taken
Only uses space for changed blocks

## Slide 44: Copy on First Write
Used by most arrays for snapshots
Used by VMware for snapshots
Used by SQL Server for snapshots
First time block is written to, old block is copied to snapshot location

## Slide 45: Copy on First Write
Data Raid Groups
Snapshot Space
Snapshot is Taken

## Slide 46: Clones
Exact duplicate of source LUN
Typically created on different physical disks
Doubles space needs

## Slide 47: A clone is a clone…
http://www.flickr.com/photos/kalexanderson/4850606898/

## Slide 48: A snapshot is a snapshot…
http://www.flickr.com/photos/unanoslucror/4577628701/

## Slide 49: A “zero copy clone” is just crap!
http://www.flickr.com/photos/editor/456743121/
Notes: Zero copy clones are just a snapshot, not a full point in time copy. So if the live version becomes corrupted, all the snapshots just become corrupted as well.

## Slide 50: Without Consistency you’ll have egg all over your face.

## Slide 51: Consistency is Key
When taking a snapshot of LUNs hosting databases all LUNs must be consistent with each other or database will be suspect.
Requires host flushes all writes to disk, and pauses all writes while snapshot is taken.

## Slide 52: With SQL we use VSS
Not Visual Source Safe, something actually useful
VSS is a Windows process, and a separate SQL Service
VSS is automatic and very reliable
VSS can be used by a storage array, or any application for software based snapshot solutions

## Slide 53: VSS Process
The array contacts VSS and queries VSS for a list of writers on the system.
  Writers are database instances, databases, physical files
Using this information the array determines which volumes should be included to get a consistent backups.
Array requests VSS create a “snap-set” of the needed LUNs
Array requests snapshot creation

## Slide 54: VSS Process
VSS instructs all writers in the snapshot to prepare for the snapshot. With SQL Server this means that a checkpoint is triggered.
When all writers report ready (all checkpoints are complete) VSS instructs writers to freeze IO, preventing new writes from being flushed to disk.
When all writers report halted, VSS instructs the hardware to create the snapshot.
  Snapshot has a 10 second timeout to complete before being canceled.
Notes: App contacts VSS and queries for the list of available Writers and their metadata (in SQL’s case there is a nested list of instances, databases, and files.)
Using this information, the app constructs the list of volumes which need to be snapped as a unit (if your database is spread across a dozen volumes, they had better all get snapshotted synchronously)
The app requests VSS to construct a “snap-set” consisting of these volumes.
The app requests snapshot creation.
VSS instructs all Writers involved in the snapshot to prepare the volumes in the set. This is non-blocking, and in SQL’s case consists of a checkpoint.
When Writers report that they are ready, VSS instructs the Writers to freeze IO to all volumes involved in the set. In SQL’s case, this means that we will stop flushing pages out of bufferpool, but pages may be read in, and all operations that can complete only touching the bufferpool, including updates, will continue unblocked. Most apps never feel the freeze.
When all apps are frozen, VSS instructs the hardware, via its Provider component, to create the snapshot set. VSS will time out this operation if it takes “too long”, which is by default 10 seconds. This timeout protects against a poorly performing hardware Provider hanging all volumes in a system.
When the hardware Provider reports that the snapshot is complete, VSS instructs all Writers to un-freeze their apps.
Apps return to normal operation.

## Slide 55: VSS Process
When the array reports that the snapshot is complete (or when VSS has timed out the snapshot) VSS instructs the writers to un-freeze the writes.
Operations return to normal.

## Slide 56: RAID isn’t a back up solution
Never assume that storage won’t fail.
Always have backups in place.
99.99% of corruption is caused by storage problems
  0.005% is bad RAM
  0.005% is SQL Bugs (excluding SQL 6.5)
If your vendor says you don’t need to backup to tape, they are lying, wrong, or stupid (or some combination)

## Slide 57: Array Based Replication
Techniques vary depending on array vendor
Most arrays can only replicate to same brand or series
  EMC to EMC
  IBM to IBM
  NetApp to NetApp
Can be done with synchronous or asynchronous
  Synchronous should have a ~100 km limit
Essentially a clone where the clone is on a different array

## Slide 58: Array Based Replication
When within a data center done over fiber channel
When between data centers done using FCoE
Take bandwidth, and latency into account when planning

## Slide 59: Synchronous Replication

## Slide 60: Asynchronous Replication

## Slide 61: Multi-Brand Replication
Typically done through a third party appliance
Usually uses switch port mirroring to capture writes from hosts to array and sends a copy of the write to a second array, often at another site.

## Slide 62: Port Mirroring

## Slide 63: MPIO Driver
Takes multiple paths and presents one disk to OS
Allows for automatic failover if path fails
Can be Active/Active or Active/Passive
Native in Windows as of Windows 2003
Native driver is free, 3rd party drivers not so much

## Slide 64: MPIO Drivers
Without MPIO Drivers
http://www.flickr.com/photos/ellipse/67038205/

## Slide 65: MPIO Drivers
With MPIO Drivers
http://www.flickr.com/photos/ellipse/67038430/

## Slide 66: Thin LUNs
Allows for over committing of storage
Allocates storage as needed when needed
Allows business to request huge amounts of storage when small amounts of storage are actually needed
Pretty much pointless for properly setup databases, great for File Servers.

## Slide 67: Monitoring
Storage arrays require monitoring
Some monitoring packages are add-on modules
Guest based monitoring (perfmon) isn’t giving you the whole story
Monitor RAID Group, LUN, Disks
Know which monitors are averages, which are maximums

## Slide 68: Monitoring

## Slide 69: Power Up / Power Down
Power Up Sequence
Power Down Sequence
Switches
Storage Array Disks
Storage Array Controller
Servers
Servers
Storage Array Controller
Storage Array Disks
Switches
http://www.flickr.com/photos/crazytales562/3146586022/

## Slide 70: Contrary to popular belief…
Not all arrays do everything well
Storage Arrays require maintenance
SANs make good NASs but NASs don’t make good SANs
Writing fast <> reading fast

## Slide 71: Storage Network Agenda
iSCSI or Fibre Channel
What needs to be redundant?
Path Count
What can be Active/Active and what can’t?
When should the switches be connected together?
Calculating network latency

## Slide 72: iSCSI VS Fibre Channel
Its about choice. The same choice doesn’t work for every situation.
http://www.flickr.com/photos/randysonofrobert/385847732/

## Slide 73: Key Differences between FC & iSCSI
Latency
  Fiber latency is measured in nano-seconds
  iSCSI is measured in mili-seconds
iSCSI uses TCP packet timeouts
Fiber cost per port is higher

## Slide 74: iSCSI Specific Settings
Jumbo Frames are a must
  Configured on Servers, Switches and Storage
Don’t cross IP subnets
Cross as few network devices as possible

## Slide 75: What needs to be Redundant?
HBAs / iSCSI NICs
Fiber Channel Switches / Network Switches
Storage Controllers
Front End Ports Array Ports
Back End Ports and Loops

## Slide 76: Redundant Fiber Channel Network

## Slide 77: Redundant iSCSI Network

## Slide 78: Redundant iSCSI Network w/ Virtualization

## Slide 79: Path Count
Each HBA has a path to each front end port on the same switch
Each iSCSI has a path to each front end port to which connectivity is granted.

## Slide 80: Fiber Channel Paths

## Slide 81: iSCSI Paths

## Slide 82: What can be Active/Active?
Yes
No
HBAs
Switches
Array Storage Processors
Single LUN Accessed through multiple switches (sometimes)
Single LUN Accessed through multiple HBAs (sometimes)
Single LUN on multiple Storage Processors (not usually)
Multiple Servers Accessing the same LUN

## Slide 83: Why Active/Active?
Greater bandwidth between server and host
4 Gig front end ports max out at 380 Mbytes / sec
8 Gig front end ports max out at 760 Mbytes / sec
Requires Active/Active MPIO driver like PowerPath on server and supporting array

## Slide 84: World Wide Name
Fiber channel equivalent of a MAC address
Every port has a WWN
WWNs can be aliased to make them readable

## Slide 85: Port Zoning
Tells the fiber switch to allow communication from one port to another
Can be done by physical ports or WWNs (or aliases)
  Physical port zoning makes replacing HBAs easier
  WWN zoning makes moving HBAs to another port easier
Most array vendors do not support single zone, zoning

## Slide 86: Port Zoning
In Windows 1 HBA is zoned to all array front end ports
In VMware 1 HBA is zoned to 1 front end ports
HBAs can be in multiple zones

## Slide 87: Connecting Switches Together
Called ISL – Inter-Switch Link
Allows equipment on one switch to access other switch
Allows for network growth without replacing equipment
Brocade/McData requires ISL License

## Slide 88: Connecting Switches Together
ISL Greatly reduces port counts
Multiple ISL ports should be on same ASIC
Always push config to switches, then activate.
Trunk ports for increased bandwidth

## Slide 89: Basic ISL Diagram

## Slide 90: ISL Diagram
Right Way
Wrong Way

## Slide 91: Reduced Port Count

## Slide 92: Calculating Network Latency
All latency is measured in one direction
  1 meter = 5 nanoseconds of latency
  100 meters = 1 microsecond
  100 kilometers = 1 millisecond
  1000 kilometers = 10 milliseconds
LA to NY = ~2778 miles = ~4470 km = 44 milliseconds
Add 2 microseconds for each ASIC change made
Keep those cables short!

## Slide 93: Site to Site
FCIP – Fiber Channel over IP
FC Router – Fiber Channel Router (optional)
  Allows switches to talk, without sharing a fabric
  Zone from primary array to FCIP Router
  Zone from secondary array to FCIP Router
Lots of bandwidth is required
Keep network latency in mind
Allows site to site array based replication

## Slide 94: Site to Site Diagram

## Slide 95: Fabric Monitoring
Switches require monitoring too
Depending on Switch MRTG may be able to be used
Some 3rd party tools exist

## Slide 96: Fabric Monitoring
Daily
Weekly
Monthly
5 Min Avg
30 Min Avg
2 Hr Avg

## Slide 97: Virtualization Agenda
Major Platform Choices
Benefits
Pitfalls
Deciding Factors
Limits of Virtualization
Management Tools
Licensing

## Slide 98: Major Platform Choices
VMware
  ESX 1-3.5
  vSphere 4.0 – 4.1
    VMware announced 4.1 will be the last version with a host console 7/30/2010
  vSphere Hypervisor (ESXi) 4.0+
Hyper-V
  V1 and v2

## Slide 99: Benefits
Hardware, Power, Cooling Costs
Instant Server Deployment
Free Server Redundancy
  Live Migration – Hyper-V
  vMotion - VMware
Easy System Upgrades
Maximizing Resource Utilization

## Slide 100: Pitfalls
Shared CPU
Shared Memory
Slow Disk Access times
Another layer of Management
Storage Path Flooding
Another layer can flush RAM to disk

## Slide 101: Deciding Factors
Disk IO
  IO Per Seconds
CPU Load
  CPU Usage
  Core Counts
  Processor Queuing
Memory Usage

## Slide 102: Disk Configuration Options
Virtual Disk (vdisk or vmdk)
  Managed by host
  Minimal Performance Impact over physical disks
  Possibly Shared with other VMs
iSCSI
  Uses network to access storage array
  Array thinks VM is a physical machine
  VM accesses Array Directly

## Slide 103: Disk Configuration Options
Pass Through (Hyper-V) or Raw Device (VMware)
  Managed by host
  Effectively gives guest direct access to Fiber Channel
Mapped HBA (VMware only)
  Maps a physical HBA directly to a VM
  HBA can only be mapped to one VM
  No vMotion, No DRS
  *Experimental*

## Slide 104: Virtualization Limits
vCPUs must be on the same physical socket
  Changed as of vSphere 4.1, requires advanced guest configuration

## Slide 105: Virtualization Limits
vMotion or Instant Failover requires hosts have like CPUs models and matching instruction sets
Hyper-V doesn’t include memory de-duplication

## Slide 106: Beware Version Limitations of VMware
VMware learned their licensing policies from the SQL Server product team.
Different editions come with different features.
  Advanced and Enterprise Plus support 12 cores
  Standard and Enterprise support 6 cores
  Enterprise Plus supports up to 8 vCPUs per VM others 4
  Enterprise and Enterprise Plus support PowerPath
  Enterprise and Enterprise Plus support DRS

## Slide 107: Memory Configurations
Give as much memory as needed to prevent swapping
  Within the Guest
  At the Host
Memory pressure at the host can force the host to reclaim memory (Balloon Driver)
  This isn’t always a bad thing
  Don’t disable the Balloon Driver
Look at the VM Memory counters

## Slide 108: Management Tools
VMware requires vCenter to manage a cluster
Hyper-V has basic management tools included, including integration with Windows Failover Cluster Manager
System Center Virtual Machine Manager (SCVMM) is strongly recommended for managing Production Environments
  SCVMM can also manage ESX 3.5 or vSphere 4.0 Servers (requires vCenter server)
  SCVMM integrates with System Center Operations Manager (SCOM) to drive SCVMM Performance Resource Optimization (PRO Tips)
  SCVMM is required for Hyper-V Physical to Virtual (P2V) migrations.
Notes: SCVMM = System Center Virtual Machine Manager

## Slide 109: vCenter Client

## Slide 110: Licensing
CAL based licensing doesn’t change
  1 Server license per guest + CALs for users
CPU licensing
  1 license for physical CPU used
  1 2008 R2 DCE CPU license for each CPU in host
  If you have SQL 2008 R1 with SA for hosts you are grandfathered into SQL 2008 R2. http://bit.ly/cGiatM
Each guest needs a Windows license
Notes: http://download.microsoft.com/download/2/7/0/270B6380-8B38-4268-8AD0-F480A139AB19/SQL2008R2_LicensingQuickReference-updated.pdf

## Slide 111: Monitoring
Monitor at all levels
  Guests
  Hosts
  Storage
Correlate the numbers together

## Slide 112: Monitoring Hosts

## Slide 113: Monitoring Hosts

## Slide 114: Monitoring the Guest
Guest CPU Load requires double checking against the host
Disk IO rates are accurate
Disk IO throughput should be confirmed with the host
Disk Latency should be confirmed with the host

## Slide 115: Beware the ParaVirtual Vmware Driver
This storage driver improves performance
Perfmon IO counters will be wrong for writes
  Driver bundles up many writes and sends one large OP
Use the VMware Disk Perfmon Counters

## Slide 116: Monitoring the Guest - CPU

## Slide 117: Monitoring the Guest - Storage

## Slide 118: Always Test Host Upgrades
A bad host upgrade could crash multiple guests
Don’t be like VMware 4.1 with 10 Gig Intel Nics
  Can cause Purple Screen of Death

## Slide 119: Build as thin a guest as possible
Remove Screensavers
Remove un-used services
Removed un-needed virtual hardware
  CD Rom, Floppy, USB, etc

## Slide 120: Q & A

## Slide 121: Who wants some free stuff?
This I’ll have to mail to you.
This I have with me.

## Slide 122: Thanks for coming
See you tomorrow at SQL Saturday.

## Slide 123: Denny Cherry
mrdenny@mrdenny.com
http://itke.techtarget.com/sql-server
http://twitter.com/mrdenny
Please fill out the survey at http://speakerrate.com/mrdenny.